## Slide 1: Indoor localization
Mehrdad Dehdashti,
Guy Lifshitz,
Shams Methnani,
Lauren Campbell,
Andrey Paunov

## Slide 2: What is it?
It is not GPS!
GPS uses satellite navigation system. Always works near the Earth’s surface! Accuracy rate 10 – 100m
Indoor locationing uses Wi-Fi, Bluetooth or special sensory

## Slide 3: Why the interest?
Mobile devices – used widely
Augmented reality – interactive video games
Campus maps (www.campusguiden.no)
Guided tours of museums
Mall and airport maps
Targeted advertising
Already there:
Microsoft’s RADAR (signal strength map of a building)
Active Bat from AT&T (ultrasonic detectors)

## Slide 4: Classification of location tracking systems

## Slide 5
Positioning aspect:
Proximity – Course grained (Rough estimation) of the target position
Angulation & Lateration – both use fine grained (precise estimations)
Variable aspect:
Received angle – between target and reference locations (angulation estimation)
Propagation time – signal transmission form transmitter to receiver (constant – used to find the distance between the target and the sensors)
Signal strength – measured at the receiver (signal strength inversely proportional to distance)

## Slide 6
Ranging aspect:
Angle of arrival (AOA), time of arrival (TOA), time difference of arrival (TDOA), improvement over TOA, and received signal strength (RSS)
Device aspect:
Antenna array – measure angle of received signal, by comparing the phase difference of signal from different antennas
Radio frequency (RF) transceiver – measure the received power and provide to RSS

## Slide 7: Algorithms
Hop – count Spreading
Triangulation Estimation
Trilateration Estimation

## Slide 8: Indoor != Outdoor Locationing
 | Outdoor | Indoor
Path loss model | Linear | Affected by multi-path and shadowing
Accuracy | Easy to achieve but not necessary (wide space) | Difficult to achieve but important (small space)
Space | Wide and not limited | Small and mostly rectangular
Deployment | Random | Can be planned
Transmission power | Maximum to maintain Location/Quantity Indicator (LQI) | Adjusted to avoid interference
Height of reference nodes | Ground | Ceiling
Map | Global | Local
Table 1: Comparison of Indoor and Outdoor Location Tracking (Pu, 2009)

## Slide 9: Advantages of using WSN for indoor locationing
Low power consumption
Inexpensive devices
No special equipment required
Software configurable and flexible
Wide radio coverage
Good processing ability
Sufficient I/O for sensing and actuating
WSN abundant set of resources

## Slide 10: Disadvantages of using WSN for indoor locationing
Sensor size constraint
Limited in processing capability
Storage capacity
Communication bandwidth
Battery power supply

## Slide 11: References
Bilton, 2012, Samsung, Nokia, and Qualcomm team up to improve indoor location technology http://venturebeat.com/2012/08/23/samsung-nokia-and-qualcomm-team-up-to-improve-indoor-location-technology/
Pu et al., Indoor Location Tracking using Received Signal Strength Indicator